“Control Logic Gates”
Group Presentation:
Team Members:
- Ujjwal Upreti
- Anish Thakuri
- Sagar Giri
- Krishna Chauhan

---
Overview:
Topics in todays presentation:
Circuit Terminology
Flow charts and tables
Examples
Conclusion

---
Circuit Terminology
Registers:
- AR - Address Register
- PC – Program Counter
- DR – Data Register
- AC – Accumulator
- IR – Instruction Register
- TR – Temporary Register
- OUTR – Output Register
- INPR – Input Register
- SC – Sequence Counter

---
Circuit Terminology (contd..)
Flip Flops
- IEN – Interrupt Enable
- FGI – Input Flag
- FGO – Output Flag
  Others:
- D0 – D7 (decoders inputs)
- T0 – T15 (Timing Control)
- INR – Increment
- CLR - Clear

---
Circuit , Flow charts and tables

---
Circuit , Flow charts and tables (contd..)
The inputs to this circuit come from the two decoders, the I flip-flop, and bits 0 through 11 of IR.
The other inputs to the control logic are: AC bits 0 through 15 to check check if AC = 0 and to detect the sign bit in AC(15); DR bits 0 through 15 to check if DR = 0; and the values of the seven flip-flops.

---
Circuit , Flow charts and tables (contd..)
The outputs of the control logic circuit are:
1. Signals to control the inputs of the nine registers
2. Signals to control the read and write inputs of memory
3. Signals to set, clear, or complement the flip-flops
4. Signals for S2, S1, and S0 to select a register for the bus
5. Signals to control the AC adder and logic circuit

---
Circuit , Flow charts and tables (contd..)

---
Examples:
R'T0: AR PC
        R'T2: AR IR(O-11)
        D7IT3: AR M[AR]
RT0: AR 0
       D5T4: AR AR + 1
These are the transfer of information from register or memory to AR.

---
Examples:
LD(AR) = R'T0 + R'T2 + D7'IT3
CLR(AR) = RT0
INR(AR) = D5T4
Read = R'T1+ D7'IT3 + (D0 + D1 + D2 + D6)T4

---
Conclusion:
- Control Logic gates is the crucial element in the design of basic computer.
- All of the algorithms and mathematics that can be described with Boolean logic
- Control Logic Gates are used to control read and write control in the memory.
- Used to trigger the flip-flops.
- Control Logic gates generates signals to control the Accumulator(AC) adder and other logical circuits that follow after Control logic gates circuit block.

---
Sources:
- Computer System Architecture (3rd Edition) – M. Morris	Mano
- Notes of Computer Architecture (CSC. 201) - Third Semester Prepared By: Arjun Singh Saud from www.bsccsit.com
- http://en.wikipedia.org/wiki/Logic_gate

---
THANK YOU